cONTRIBUTION:	nTCOxxx.doc	 2000 06 12

working Group:	Network Working Group

title:			Location Information in Roaming

Issues Addressed:	This contribution provides comments to Clearnet's proposed solutions in NTCO087.doc

Source:	Bell Canada	
Tony Chow  	 		Douglas Kwong

Rm. 970,			Rm. 630,

160 Elgin St.

Ottawa, Ontario

Tel: 613-781-8508		Tel: 613-781-5388

Anthony.chow@bell.ca  	douglas.kwong@bell.ca

Distribution:	NTWG Interested Parties

REFERENCE:

FILE NAME:

Notice:	This contribution has been prepared by Bell Canada to assist the Network Working Group as basis for discussion. This should not be construed as a binding proposal on Bell Canada. Specifically, Bell Canada reserves the right to request amendments, modifications or to withdraw of this contribution at any time.

Introduction:

One of the issues raised at the CISC Network WG (NTWG) on wireless CLEC is that IXCs require location information to rate and bill LD calls made by a roaming wireless CLEC subscriber.  At the May 2 NTWG meeting, Clearnet proposed 3 solutions to this issue. The purpose of this contribution is to provide comments on Clearnet's proposed solutions.

Clearnet's Proposed Solutions*

- The generation of specific IXSP rate plans in order to accommodate for any ambiguity in the location of the subscriber (e.g. a flat-rate plan)

- Provision of Call Detail Records (CDRs) from the LEC to facilitate the IXSP's downstream billing process (Note: Clearnet indicated verbally that it would be flexible as to the format of the CDR)

- (Long Term) Modification of FG-D/TR394 protocol to provide incremental location information to the IXC. Note that existing standards and specifications provide for the identification of the originating end-office via the Jurisdictional Information Parameter (JIP).

Comments on the Proposed Solutions

Solution 1:	Outside the scope of the Network WG

Solution 2:	Significant development will be required in the downstream billing systems to accommodate location information in order to properly rate and bill these LD calls. The interim solution (item 2 above) proposed by Clearnet is non-standard (or may not be applicable to other Wireless CLECs) and will result in throwaway development effort. CISC should not encourage the development and adoption of non-standard method, proposed by Clearnet for use by industry.

Solution 3:	Bell recommends that the NTWG should investigate standard methods such as the use of JIP parameter to capture location information.

* NTWG contribution NTCO087.doc